The Second Experiment
Checking very carefully all aspects of the apparatus and how the core is confined to ensure that no confining fluid enters the core. Checking backpressure and using production regulator.

Experimental procedure and displacement sequence:
1.	Injecting water at different rates.
2.	Measuring pressure drop and calculating permeability for single-phase flow.
3.	Oil is injected as the second phase of the sample.
4.	Water and oil are injected to reach a steady-state condition between oil and water.
5.	Measuring pressure drop for two-phase flow.
6.	Checking the results to identify anything that appears unexpected.
7.	Water, oil and gas then simultaneously are injected.
8.	Increasing the total flow rate, keeping the fractional flows the same.
9. use the less fraction flow for the gas compared to the oil and water fraction that Abdulla used in his experiment.

Fractional flow can be introduced as below,
Flooding step	fw	fo	fg	Qw	Qo	Qg
				ml/min	ml/min	ml/min
1	1	0	0	1, 0.05,0.8	0	0
2	0	1	0	0	0.1	0
3	0.5	0.5	0	0.05	0.05	0
4	0.375	0.375	0.25	0.025	0.025	0.05
5				0.05	0.05	0.1
6				0.1	0.1	0.2
7				0.2	0.2	0.4